## Slide 1: Hardware Simulation and Software Models for P1687.1 and P2654
Bradford G. Van Treuren 18 July 2019

## Slide 2: Overview
A hardware simulation environment to experiment with ideas conforming to standards development
A generalized software interface to the simulation environment allowing access from any language
Published ideas of methodologies implementing standards concepts as examples of implementation
Allow experimentation of different ideas to benchmark benefits and consequences of ideas

## Slide 3: Goal of Project
Provide a simulation environment consisting of various technologies implemented by a hierarchical topography
Model instruments using hardware test standards as the interface to the instruments
Provide a language independent interface to the simulated environment
Support testing of device and/or board designs in the simulator
Provide software examples for implementing strategies supporting P1687.1 and P2654

## Slide 4: High Level Interface Architecture
myHDL Simulation
Telnet Server
Simulated Bus Interface
JTAG
GPIO
I2C
SPI
Host Test Bus Interfaces
Other
Telnet Client
Telnet Client
Telnet Client
C/C++ App
Virtual Drivers
Python App
Virtual Drivers
TCL App
Virtual Drivers
Wishbone, etc.
MEMWRITE
MEMREAD

## Slide 5: Device Testing
Python myHDL Simulation
IP_2 Core From Rearick Use Case Model
IP_2
1687 I/F
SIB2
SIB1
PowerSupplyMonitor
NoiseMaker
SI1
IEEE 1149.1 JTAG TAP Controller
Pin IF
IEEE 1149.1 JTAG TAP Master Controller
TDI
TCK
TMS
TRST
TDO
WISHBONE
Simulated Bus Interface Software Test Bench
Telnet Server Command Interface to Wishbone Bus
Telnet Client
C++ SimDrvr
SimDrvr Python
DATA
STARTSTATE
ENDSTATE
BITCOUNT
CNTRL/STAT
MEMWRITE
MEMREAD
MEMWRITE
MEMREAD

## Slide 6: Board Testing
Python myHDL Simulation
IEEE 1149.1 JTAG TAP Master Controller
TDI
TCK
TMS
TRST
TDO
WISHBONE
Simulated Bus Interface Software Test Bench
Telnet Server Command Interface to Wishbone Bus
Telnet Client
C++ SimDrvr
SimDrvr Python
DATA
STARTSTATE
ENDSTATE
BITCOUNT
CNTRL/STAT
MEMWRITE
MEMREAD
MEMWRITE
MEMREAD
Pin IF
Scan Path Linker
JTAG TO I2C BRIDGE
JTAG TO SPI BRIDGE
JTAG DEVICE ONE
JTAG DEVICE TWO
JTAG DEVICE THREE
SPI DEVICE ONE
I2C DEVICE ONE
JTAG

## Slide 7: Complex Board Testing
Python myHDL Simulation
TAP Controller
WISHBONE
Simulated Bus Interface Software Test Bench
Telnet Server Command Interface to Wishbone Bus
Telnet Client
C++ SimDrvr
SimDrvr Python
MEMWRITE
MEMREAD
MEMWRITE
MEMREAD
Pin IF
Scan Path Linker
JTAG TO I2C BRIDGE
JTAG TO SPI BRIDGE
JTAG DEVICE ONE
JTAG DEVICE TWO
JTAG DEVICE THREE
SPI DEVICE ONE
I2C DEVICE ONE
JTAG
I2C Controller
I2C DEVICE TWO

## Slide 8: Example: MBIST with temperature feedback
MBIST4
MBIST2
MBIST3
BYP
Thermometer + Comparator
IP_3
1687 I/F
SIB2
SIB1
WIR
reg
LED
SIB3
WDRmux
WIR mux
SELWIR
MBIST5
mux
IP_2
1687 I/F
SIB2
SIB1
PowerSupplyMonitor
NoiseMaker
Transform engine
1687 portal register
func register 1
func register i
.
.
.
IP_1
func register 2
Functional registers
. . .
SI2
SI1
MBIST1
API
device i
Interface i2
Interface i1
Communication Interface
…
Functional _Instruments
…
DPIC (I2C)
…
Functional _Instruments
DI1
The simple example test:
Start MBIST
While MBIST runs, read the temperature
If the temperature is too high, stop MBIST
Otherwise run the MBIST until it is done
Read the result
Rearick Use Case Model

## Slide 9: Board Models

## Slide 10: Client Models

## Slide 11: I2CClient Entity

## Slide 12: I2CClient Entity I2C Slave Interface
parent
name
For myHDL debugging
reset_n
scl_i
sda_t
sda_i
device_address
write_address
write_data
read_address
read_data
sda_o
update
capture
sda
VCC
scl
VCC

## Slide 13: Common Models

## Slide 14: ScanRegister Entity

## Slide 15: ScanRegister Entity
so
parent
name
For myHDL debugging
si
ce
se
ue
sel
reset
clock
di
width
do

## Slide 16: ScanRegister Entity
def ScanRegister(path, name, si, ce, se, ue, sel, reset, clock, so, di, do, width=9, monitor=False):
"""
Generic ScanRegister design following the Capture/Shift/Update protocol
:param path: Dot path of the parent of this instance
:param name: Instance name for debug logger (path instance)
:param si: ScanIn Port
:param ce: CaptureEnable Port
:param se: ShiftEnable Port
:param ue: UpdateEnable Port
:param sel: Select Port
:param reset: Reset Port
:param clock: Clock Port
:param so: ScanOut Port
:param di: DataIn Port
:param do: DataOut Port
:param width: The number of bits contained in this register
:param monitor: False=Do not turn on the signal monitors, True=Turn on the signal monitors
"""

## Slide 17: InstructionRegister Entity

## Slide 18: InstructionRegister Entity
parent
name
For myHDL debugging
si
ce
so
se
ue
sel
reset
clock
di
width
do

## Slide 19: InstructionRegister Entity
def InstructionRegister(path, name, si, ce, se, ue, sel, reset, clock, so, di, do, width=9, monitor=False):
"""
Generic InstructionRegister design following the Capture/Shift/Update protocol
:param path: Dot path of the parent of this instance
:param name: Instance name for debug logger (path instance)
:param si: ScanIn Port
:param ce: CaptureEnable Port
:param se: ShiftEnable Port
:param ue: UpdateEnable Port
:param sel: Select Port
:param reset: Reset Port
:param clock: Clock Port
:param so: ScanOut Port
:param di: DataIn Port
:param do: DataOut Port
:param width: The number of bits contained in this register
:param monitor: False=Do not turn on the signal monitors, True=Turn on the signal monitors
"""

## Slide 20: RAM Entity

## Slide 21: RAM Entity
din
dout
depth
addr
we
clk

## Slide 22: RAM Entity
@block
def ram(dout, din, addr, we, clk, depth=128):
""" Ram model """
mem = [Signal(intbv(0)[8:]) for i in range(depth)]
@always(clk.posedge)
def write():
if we:
mem[addr].next = din
@always_comb
def read():
dout.next = mem[addr]
return write, read

## Slide 23: ROM Entity

## Slide 24: ROM Entity
addr
data
CONTENT
Tuple of Read-Only Data Values as Integers

## Slide 25: ROM Entity
CONTENT = (17, 134, 52, 9)
@block
def rom(dout, addr, CONTENT):
""" ROM model """
@always_comb
def read():
dout.next = CONTENT[int(addr)]
return read

## Slide 26: Controllers Models

## Slide 27: Cores Models

## Slide 28: IP_1 Entity From Rearick Use Case Model
clk
o_clock_freq
reset_n
parent
name
For myHDL debugging
count_max
Functional _Instruments
…
…
Functional _Instruments
DI1
Clock Generator
Frequency Counter
16
8

## Slide 29: IP_2 Entity From Rearick Use Case Model
ijtag_si
ijtag_so
IP_2
1687 I/F
SIB2
SIB1
PowerSupplyMonitor
NoiseMaker
ijtag_interface
parent
name
For myHDL debugging
pu_mbist1-5
fast_ck
ck

## Slide 30: Device Models
Bridges

## Slide 31: TPSP Entity From Martin Keim Use Case Model
reset_n
spio_in
parent
name
For myHDL debugging
tdo
jtag_interface
spio_en
spio_out
spclk
tdo_en
tdi
power_usage_ register
thermal_ register

## Slide 32: SPItoI2C Entity From OpenCores.com Model
clock
sclk
parent
name
For myHDL debugging
trdy
scl
sda
mosi
ss_n
miso
reset_n

## Slide 33: Device Models
Use Cases

## Slide 34: Device Models
Hosts

## Slide 35: JTAGCtrlMaster Entity From OpenCores.com Model
clk
tdo
parent
name
For myHDL debugging
trdy
jtag_interface
tdi
bit_count
dout
reset_n
16
state_end
4
state_start
4
addr
10
din
8
wr
8
Vector BRAM
TAP Controller
State Machine
addr_width=10
data_width=8

## Slide 36: Instrument Models

## Slide 37: Simulated MBIST Instrument

## Slide 38: Simulated MBIST Instrument
clock
initialize_delay=10
thermal_register(0-100)
power_usage_register(0-100)
status_register[0:7]
control_register[0:7]
reset_n
analyze_delay=20
test_delay=30
MBIST FSM
START
INITIALIZE
IDLE
INITIALIZE
DELAY
TEST
TEST DELAY
ANALYZE
ANALYZE DELAY
POWER PRESETS
IDLE=5
START=10
INIT=30
TEST=100
ANALYZE=70
THERMAL PRESETS
IDLE=5
START=10
INIT=30
TEST=100
ANALYZE=70
parent
name
For myHDL debugging

## Slide 39: MBIST Simulation State Machine
START
INITIALIZE
IDLE
INITIALIZE
DELAY
TEST
TEST DELAY
ANALYZE
ANALYZE DELAY
Entrance State
Control Start Bit moves to here
Simulating setup operations
Wait N clock ticks to simulate initialization
Simulating memory test operations
Wait N clock ticks to simulate testing
Simulating analysis operations
Wait N clock ticks to simulate analyzing

## Slide 40: MBIST Control Register
Bit | Signal Name | Description
6 | analyze_wait | 1=Double the analyze_delay time to use at start, 0=Use the specified analyze_delay
5 | test_wait | 1=Double the test_delay time to use at start, 0=Use the specified test_delay
4 | initialize_wait | 1=Double the initialize_delay time to use at start, 0=Use the specified initialize_delay
3 | inj_analyze_err | 1=Inject error during analyze_delay state, 0=Do not inject error during analyze_delay state
2 | inj_test_err | 1=Inject error during test_delay state, 0=Do not inject error during test_delay state
1 | abort | 1=Stop the BIST operation and abort, 0=Do not abort the test
0 | start | 1=Start the BIST operation, 0=NOP for status scans

## Slide 41: MBIST Status Register
Bit | Signal Name | Description
6 | Reserved1 | Reserved. Added so status_register can be capture register and control_register as update
5 | Reserved0 | Reserved. Added so status_register can be capture register and control_register as update
4 | analyze_error | 1=Error during analyze state detected, 0=No error detected during analyze state
3 | test_error | 1=Error during test state detected, 0=No error detected during test state
2 | unknown_error | 1=Test aborted due to unknown error, 0=Test did not abort
1 | status | 1=MBIST test is running, 0=MBIST test is not running
0 | result | 1=Test passed, 0=Test failed

## Slide 42: MBIST Power Usage
power_usage_register (intbv, min=0, max=101)
Percentage of allocated power for each step
Built-in preset values for each step of operation
  IDLE=5
  START=10
  INIT=30
  TEST=100
  ANALYZE=70
Value output used with power manager to calculate a simulated power load for the whole board

## Slide 43: MBIST Temperature Usage
thermal_register (intbv, min=0, max=101)
Percentage of allocated thermal rating for each step
Built-in preset values for each step of operation
  IDLE=5
  START=10
  INIT=30
  TEST=100
  ANALYZE=70
Value output used with temperature monitor to calculate a simulated power load for the whole board

## Slide 44: LED Instrument

## Slide 45: LED Simulated Instrument
parent
name
For myHDL debugging
di

## Slide 46: LED Data Register
Bit | Signal Name | Description
0 | di | Data input port: 1=ON, 0=OFF

## Slide 47: Thermometer Instrument

## Slide 48: Thermometer Simulated Instrument
parent
name
For myHDL debugging
temperature
thermal_register1
thermal_register2
thermal_register3
thermal_register4
thermal_register5
clock
reset_n
From MBIST Instruments

## Slide 49: Thermometer thermal_registerX Register
Bit | Signal Name | Description
7 | MSB | Most Significant Bit of thermal_register from MBISTX.
6 | bit6 | Data bit of thermal_register from MBISTX.
5 | bit5 | Data bit of thermal_register from MBISTX.
4 | bit4 | Data bit of thermal_register from MBISTX.
3 | bit3 | Data bit of thermal_register from MBISTX.
2 | bit2 | Data bit of thermal_register from MBISTX.
1 | bit1 | Data bit of thermal_register from MBISTX.
0 | LSB | Least Significant Bit of thermal_register from MBISTX.

## Slide 50: Thermometer Temperature Register
Bit | Signal Name | Description
8 | MSB | Most Significant Bit of Temperature in Fahrenheit.
7 | bit7 | Data bit of Temperature in Fahrenheit.
6 | bit6 | Data bit of Temperature in Fahrenheit.
5 | bit5 | Data bit of Temperature in Fahrenheit.
4 | bit4 | Data bit of Temperature in Fahrenheit.
3 | bit3 | Data bit of Temperature in Fahrenheit.
2 | bit2 | Data bit of Temperature in Fahrenheit.
1 | bit1 | Data bit of Temperature in Fahrenheit.
0 | LSB | Least Significant Bit of Temperature in Fahrenheit.

## Slide 51: Comparator Instrument

## Slide 52: Comparator Instrument
parent
name
For myHDL debugging
clock
reset_n
temperature
low_register
high_register
status_register

## Slide 53: Comparator Temperature Register
Bit | Signal Name | Description
8 | MSB | Most Significant Bit of Temperature in Fahrenheit.
7 | bit7 | Data bit of Temperature in Fahrenheit.
6 | bit6 | Data bit of Temperature in Fahrenheit.
5 | bit5 | Data bit of Temperature in Fahrenheit.
4 | bit4 | Data bit of Temperature in Fahrenheit.
3 | bit3 | Data bit of Temperature in Fahrenheit.
2 | bit2 | Data bit of Temperature in Fahrenheit.
1 | bit1 | Data bit of Temperature in Fahrenheit.
0 | LSB | Least Significant Bit of Temperature in Fahrenheit.

## Slide 54: Comparator low_register Register
Bit | Signal Name | Description
8 | MSB | Most Significant Bit of low_register Temperature in Fahrenheit.
7 | bit7 | Data bit of low_register Temperature in Fahrenheit.
6 | bit6 | Data bit of low_register Temperature in Fahrenheit.
5 | bit5 | Data bit of low_register Temperature in Fahrenheit.
4 | bit4 | Data bit of low_register Temperature in Fahrenheit.
3 | bit3 | Data bit of low_register Temperature in Fahrenheit.
2 | bit2 | Data bit of low_register Temperature in Fahrenheit.
1 | bit1 | Data bit of low_register Temperature in Fahrenheit.
0 | LSB | Least Significant Bit of low_register Temperature in Fahrenheit.

## Slide 55: Comparator high_register Register
Bit | Signal Name | Description
8 | MSB | Most Significant Bit of high_register Temperature in Fahrenheit.
7 | bit7 | Data bit of high_register Temperature in Fahrenheit.
6 | bit6 | Data bit of high_register Temperature in Fahrenheit.
5 | bit5 | Data bit of high_register Temperature in Fahrenheit.
4 | bit4 | Data bit of high_register Temperature in Fahrenheit.
3 | bit3 | Data bit of high_register Temperature in Fahrenheit.
2 | bit2 | Data bit of high_register Temperature in Fahrenheit.
1 | bit1 | Data bit of high_register Temperature in Fahrenheit.
0 | LSB | Least Significant Bit of high_register Temperature in Fahrenheit.

## Slide 56: Comparator Status Register
Bit | Signal Name | Description
7 | Reserved7 | Reserved. Added to pad read to 8 bits.
6 | Reserved6 | Reserved. Added to pad read to 8 bits.
5 | Reserved5 | Reserved. Added to pad read to 8 bits.
4 | Reserved4 | Reserved. Added to pad read to 8 bits.
3 | Reserved3 | Reserved. Added to pad read to 8 bits.
2 | Reserved2 | Reserved. Added to pad read to 8 bits.
1 | above | 1=Temperature above high value, 0=Temperature at or below high value
0 | below | 1=Temperature fell below low value, 0=Temperature at or above low value

## Slide 57: Clock Frequency Counter Instrument

## Slide 58: Clock Frequency Counter Instrument
parent
name
For myHDL debugging
clock
reset_n
o_clock_freq
16
i_clk_test

## Slide 59: Clock Frequency Counter o_clock_freq Register
Bit | Signal Name | Description
15 | MSB | Most Significant Bit of frequency in Hz.
14 | Bit14 | Bit of frequency in Hz.
13 | Bit13 | Bit of frequency in Hz.
12 | Bit12 | Bit of frequency in Hz.
11 | Bit11 | Bit of frequency in Hz.
10 | Bit10 | Bit of frequency in Hz.
9 | Bit9 | Bit of frequency in Hz.
8 | Bit8 | Bit of frequency in Hz.
7 | Bit7 | Bit of frequency in Hz.
6 | Bit6 | Bit of frequency in Hz.
5 | Bit5 | Bit of frequency in Hz.
4 | Bit4 | Bit of frequency in Hz.
3 | Bit3 | Bit of frequency in Hz.
2 | Bit2 | Bit of frequency in Hz.
1 | Bit1 | Bit of frequency in Hz.
0 | LSB | Least Significant Bit of frequency in Hz.

## Slide 60: Clock Generator Instrument

## Slide 61: Clock Generator Instrument
parent
name
For myHDL debugging
clock
reset_n
max_count
clock_pulse
min_bits

## Slide 62: Power Supply Monitor Instrument

## Slide 63: Power Supply Monitor Instrument
parent
name
For myHDL debugging
reference
delta
VDD
fast_ck
pu_mbist1
noise
pu_mbist2
pu_mbist5
pu_mbist3
pu_mbist4
over
under
noise_flag

## Slide 64: Power Supply Monitor reference Register Reference value of what the power supply voltage should be as a Signal(intbv(0)[16:]) type. Setting the reference value to zero (0) will reset the under and over signals.
Bit | Signal Name | Description
15 | MSB | Most Significant Bit of reference voltage in millivolts.
14 | Bit14 | Bit of reference voltage in millivolts.
13 | Bit13 | Bit of reference voltage in millivolts.
12 | Bit12 | Bit of reference voltage in millivolts.
11 | Bit11 | Bit of reference voltage in millivolts.
10 | Bit10 | Bit of reference voltage in millivolts.
9 | Bit9 | Bit of reference voltage in millivolts.
8 | Bit8 | Bit of reference voltage in millivolts.
7 | Bit7 | Bit of reference voltage in millivolts.
6 | Bit6 | Bit of reference voltage in millivolts.
5 | Bit5 | Bit of reference voltage in millivolts.
4 | Bit4 | Bit of reference voltage in millivolts.
3 | Bit3 | Bit of reference voltage in millivolts.
2 | Bit2 | Bit of reference voltage in millivolts.
1 | Bit1 | Bit of reference voltage in millivolts.
0 | LSB | Least Significant Bit of reference voltage in millivolts.

## Slide 65: Power Supply Monitor Status Register over: Signal to indicate the monitor detected the voltage exceeded the delta setting. Signal(bool(0)) type. under: Signal to indicate the monitor detected the voltage fell below the delta setting. Signal(bool(0)) type.
Bit | Signal Name | Description
1 | over | Signal to indicate the monitor detected the voltage exceeded the delta setting. Signal(bool(0)) type.
0 | under | Signal to indicate the monitor detected the voltage fell below the delta setting. Signal(bool(0)) type.

## Slide 66: Power Supply Monitor noise_flag Register noise_flag: Signal to enable or disable noise influence on Power Supply Monitoring. Signal(bool(1)) type.
Bit | Signal Name | Description
0 | noise_flag | Signal to enable(1) or disable(0) noise influence on Power Supply Monitoring. Signal(bool(1)) type.

## Slide 67: Power Supply Monitor delta Register The amount of mV variance allowed around the voltage reference as a Signal(intbv(0)[8:]) type.
Bit | Signal Name | Description
7 | MSB | Most Significant Bit of delta register.
6 | Bit6 | Bit of delta register.
5 | Bit5 | Bit of delta register.
4 | Bit4 | Bit of delta register.
3 | Bit3 | Bit of delta register.
2 | Bit2 | Bit of delta register.
1 | Bit1 | Bit of delta register.
0 | LSB | Least Significant Bit of delta register.

## Slide 68: Noise Maker Instrument

## Slide 69: Noise Maker Instrument
parent
name
For myHDL debugging
num_toggles
num_stages
ck
noise
8

## Slide 70: Noise Maker num_toggles Register Number of toggles to perform per stage. Signal(intbv(0, min=0, max=MAX_TOGGLES))
Bit | Signal Name | Description
4 | MSB | Most Significant Bit of num_toggles register.
3 | Bit3 | Bit of num_toggles register.
2 | Bit2 | Bit of num_toggles register.
1 | Bit1 | Bit of num_toggles register.
0 | LSB | Least Significant Bit of num_toggles register.

## Slide 71: Noise Maker num_stages Register Number of stages to perform per clock cycle. Signal(intbv(0, min=0, max=MAX_STAGES))
Bit | Signal Name | Description
3 | MSB | Most Significant Bit of num_stages register.
2 | Bit2 | Bit of num_stages register.
1 | Bit1 | Bit of num_stages register.
0 | LSB | Least Significant Bit of num_stages register.

## Slide 72: Standard’s Models
IEEE P1687.1

## Slide 73: Standard’s Models
IEEE Std 1149.1

## Slide 74: Std1149_1_TAP Entity
parent
name
For myHDL debugging
jtag_interface
tap_interface
state (DCBA code)

## Slide 75: Test Data Register (TDR)
parent
name
For myHDL debugging
tap_interface
D
Q
scan_in
scan_out
tck
local_reset
select
tdr_width

## Slide 76: Test Instruction Register (TIR)
scan_out
parent
name
For myHDL debugging
tap_interface
D
Q
scan_in
tck
local_reset
select
tir_width

## Slide 77: Standard’s Models
IEEE Std 1500

## Slide 78: Select WIR (SELWIR)
so
parent
name
For myHDL debugging
ijtag_interface
select_wir
si

## Slide 79: Wrapper Bypass (WBY)
wby_wso
parent
name
For myHDL debugging
wsp_interface
select_wir
wsi
select
width

## Slide 80: Wrapper Data Register MUX(WDRMUX)
parent
name
For myHDL debugging
wsp_interface
so
mbist1_out
mbist2_out
wby_out
mbist3_out
wr_select_list
dr_select_list

## Slide 81: Wrapper Instruction Register (WIR)
parent
name
For myHDL debugging
wsi
wso
wr_list
user_list
wsp
wr_select_list
dr_select_list

## Slide 82: Wrapper Instruction Register MUX(WIRMUX)
parent
name
For myHDL debugging
wdr_out
so
select_wir
wir_out

## Slide 83: Wrapper ScanRegister (WSREG)
parent
name
For myHDL debugging
si
so
select
wsp_interface
di
dr_width
do

## Slide 84: Standard’s Models
IEEE Std 1687

## Slide 85: SIB MUX POST
parent
name
For myHDL debugging
si
so
from_so
from_ijtag_interface
to_si
to_ijtag_interface

## Slide 86: SIB MUX PRE
parent
name
For myHDL debugging
si
so
from_so
from_ijtag_interface
to_si
to_ijtag_interface

## Slide 87: Standard’s Models
IEEE P2654